## Slide 1: Computer Organization and Architecture Designing for Performance
11th Edition
Chapter 19
Control Unit Operation and Microprogrammed Control

## Slide 2: Micro-Operations
The functional, or atomic, operations of a processor
Series of steps, each of which involves the processor registers
Micro refers to the fact that each step is very simple and accomplishes very little
The execution of a program consists of the sequential execution of instructions
  Each instruction is executed during an instruction cycle made up of shorter subcycles (fetch, indirect, execute, interrupt)
  The execution of each subcycle involves one or more shorter operations (micro-operations)
Notes: We have seen that the operation of a computer, in executing a program, consists of a
sequence of instruction cycles, with one machine instruction per cycle. Of course, we
must remember that this sequence of instruction cycles is not necessarily the same
as the written sequence of instructions that make up the program, because of the
existence of branching instructions. What we are referring to here is the execution
time sequence of instructions.
We have further seen that each instruction cycle is made up of a number of
smaller units. One subdivision that we found convenient is fetch, indirect, execute,
and interrupt, with only fetch and execute cycles always occurring.
To design a control unit, however, we need to break down the description
further. In our discussion of pipelining in Chapter 16, we began to see that a further
decomposition is possible. In fact, we will see that each of the smaller cycles
involves a series of steps, each of which involves the processor registers. We will
refer to these steps as micro-operations. The prefix micro refers to the fact that each
step is very simple and accomplishes very little,
Micro-operations are the functional, or atomic, operations of a processor. In this
section, we will examine micro-operations to gain an understanding of how the events
of any instruction cycle can be described as a sequence of such micro-operations.
A simple example will be used. In the remainder of this chapter, we then show how the
concept of micro-operations serves as a guide to the design of the control unit.

## Slide 3: Figure 19.1 Constituent Elements of a Program Execution
Notes: Figure 19.1 depicts the relationship
among the various concepts we have been discussing. To summarize, the execution
of a program consists of the sequential execution of instructions. Each instruction
is executed during an instruction cycle made up of shorter subcycles (e.g., fetch,
indirect, execute, interrupt). The execution of each subcycle involves one or more
shorter operations, that is, micro-operations.

## Slide 4: The Fetch Cycle
Occurs at the beginning of each instruction cycle and causes an instruction to be fetched from memory
Four registers are involved:
  Memory Address Register (MAR)
    Connected to address bus
    Specifies address for read or write operation
  Memory Buffer Register (MBR)
    Connected to data bus
    Holds data to write or last data read
  Program Counter (PC)
    Holds address of next instruction to be fetched
  Instruction Register (IR)
    Holds last instruction fetched
Notes: We begin by looking at the fetch cycle, which occurs at the beginning of each instruction
cycle and causes an instruction to be fetched from memory. For purposes of
discussion, we assume the organization depicted in Figure 16.5 (Data Flow, Fetch
Cycle). Four registers are involved:
■ Memory address register (MAR): Is connected to the address lines of the system
bus. It specifies the address in memory for a read or write operation.
■ Memory buffer register (MBR): Is connected to the data lines of the system bus.
It contains the value to be stored in memory or the last value read from memory.
■ Program counter (PC): Holds the address of the next instruction to be
fetched.
■ Instruction register (IR): Holds the last instruction fetched.

## Slide 5: Figure 19.2 Sequence of Events, Fetch Cycle
Notes: Let us look at the sequence of events for the fetch cycle from the point of view of its effect on the processor registers. An example appears in Figure 19.2.
At the beginning of the fetch cycle, the address of the next instruction to be executed is in the program counter (PC); in this case, the address is 1100100.
The first step is to move that address to the memory address register (MAR) because this is the only register connected to the address lines of the system bus.
The second step is to bring in the instruction.
  The desired address (in the MAR) is placed on the address bus, the control unit issues a READ command on the control bus, and the result appears on the data bus and is copied into the memory buffer register (MBR).
  We also need to increment the PC by the instruction length to get ready for the next instruction.
  Because these two actions (read word from memory, increment PC) do not interfere with each other, we can do them simultaneously to save time.
The third step is to move the contents of the MBR to the instruction register (IR).
  This frees up the MBR for use during a possible indirect cycle.
Thus, the simple fetch cycle actually consists of three steps and four micro-operations.
Each micro-operation involves the movement of data into or out of a register.
So long as these movements do not interfere with one another, several of them can take place during one step, saving time.

## Slide 6
 | Micro-operations | 
Fetch: | t1: MAR ← (PC) | 
 | t2: MBR ← Memory PC ← (PC) + 1 | 
 | t3: IR ← (MBR) | 
Indirect: | t1: MAR ← (IR(Address)) | 
 | t2: MBR ← Memory | 
 | t3: IR(Address) ← (MBR(Address)) | 
Interrupt: | t1: MBR ← (PC) | 
 | t2 : MAR ← Save-address PC ← Routine-address | 
 | t3: Memory ← (MBR) | 
Notes: The control unit must maintain knowledge of where it is in the instruction cycle.
Using this knowledge, and by reading all of its inputs, the control unit emits a sequence of control signals that causes micro-operations to occur.
It uses the clock pulses to time the sequence of events, allowing time between events for signal levels to stabilize.
See slide 15 first.
Table 19.1 indicates the control signals that are needed for
some of the micro-operation sequences described earlier. For simplicity, the data
and control paths for incrementing the PC and for loading the fixed addresses into
the PC and MAR are not shown.
It is worth pondering the minimal nature of the control unit. The control unit
is the engine that runs the entire computer. It does this based only on knowing the
instructions to be executed and the nature of the results of arithmetic and logical
operations (e.g., positive, overflow, etc.). It never gets to see the data being processed
or the actual results produced. And it controls everything with a few control
signals to points within the processor and a few control signals to the system bus.

## Slide 7: Indirect Cycle
Once an instruction is fetched, the next step is to fetch source operands
Assuming a one-address instruction format, with direct and indirect addressing allowed:
  If the instruction specifies an indirect address, then an indirect cycle must precede the execute cycle
  The address field of the instruction is transferred to the MAR
  This is then used to fetch the address of the operand
  Finally, the address field of the IR is updated from the MBR, so that it now contains a direct rather than an indirect address
  The IR is now in the same state as if indirect addressing had not been used, and it is ready for the execute cycle
Notes: Once an instruction is fetched, the next step is to fetch source operands.
Continuing our simple example, let us assume a one-address instruction format, with direct and indirect addressing allowed.
If the instruction specifies an indirect address, then an indirect cycle must precede the execute cycle.
The data flow differs somewhat from that indicated in Figure 16.6 (Data Flow, Indirect Cycle) and includes the following micro-operations:
t1: MAR  (IR(Address))
t2: MBR  Memory
t3: IR(Address)  (MBR(Address))
The address field of the instruction is transferred to the MAR.
This is then used to fetch the address of the operand.
Finally, the address field of the IR is updated from the MBR, so that it now contains a direct rather than an indirect address.
The IR is now in the same state as if indirect addressing had not been used, and it is ready for the execute cycle.
We skip that cycle for a moment, to consider the interrupt cycle.

## Slide 8: Interrupt Cycle
At the completion of the execute cycle, a test is made to determine whether any enabled interrupts have occurred, and if so, the interrupt cycle occurs
The nature of this cycle varies greatly from one machine to another
In a simple sequence of events:
  In the first step the contents of the PC are transferred to the MBR so that they can be saved for return from the interrupt
  Then the MAR is loaded with the address at which the contents of the PC are to be saved, and the PC is loaded with the address of the start of the interrupt-processing routine
    These two actions may each be a single micro-operation
    Because most processors provide multiple types and/or levels of interrupts, it may take one or more additional micro-operations to obtain the Save_Address and the Routine_Address before they can be transferred to the MAR and PC respectively
  Once this is done, the final step is to store the MBR, which contains the old value of the PC, into memory
  The processor is now ready to begin the next instruction cycle
Notes: At the completion of the execute cycle, a test is made to determine whether any enabled interrupts have occurred.
If so, the interrupt cycle occurs. The nature of this cycle varies greatly from one machine to another.
We present a very simple sequence of events, as illustrated in Figure 16.7(Data Flow, Indirect Cycle). We have
t1: MBR  (PC)
t2: MAR  Save_Address
PC  Routine_Address
t3: Memory  (MBR)
In the first step, the contents of the PC are transferred to the MBR, so that they can be saved for return from the interrupt.
Then the MAR is loaded with the address at which the contents of the PC are to be saved, and the PC is loaded with the address of the start of the interrupt-processing routine.
These two actions may each be a single micro-operation.
However, because most processors provide multiple types and/or levels of interrupts, it may take one or more additional micro-operations to obtain the Save_Address and the Routine_Address before they can be transferred to the MAR and PC, respectively.
In any case, once this is done, the final step is to store the MBR, which contains the old value of the PC, into memory.
The processor is now ready to begin the next instruction cycle.

## Slide 9: Execute Cycle
Because of the variety of opcodes, there are a number of different sequences of micro-operations that can occur
Instruction decoding
  The control unit examines the opcode and generates a sequence of micro-operations based on the value of the opcode
A simplified add instruction:
  ADD R1, X (which adds the contents of the location X to register R1)
    In the first step the address portion of the IR is loaded into the MAR
    Then the referenced memory location is read
    Finally the contents of R1 and MBR are added by the ALU
    Additional micro-operations may be required to extract the register reference from the IR and perhaps to stage the ALU inputs or outputs in some intermediate registers
Notes: The fetch, indirect, and interrupt cycles are simple and predictable.
Each involves a small, fixed sequence of micro-operations and, in each case, the same micro-operations are repeated each time around.
This is not true of the execute cycle. Because of the variety of opcodes, there are a number of different sequences of micro-operations that can occur.
The control unit examines the opcode and generates a sequence of micro-operations based on the value of the opcode. This is referred to as instruction decoding.
Let us consider several hypothetical examples.
First, consider an add instruction:
ADD R1, X
which adds the contents of the location X to register R1. The following sequence of
Micro-operations might occur:
t1: MAR  (IR(address))
t2: MBR  Memory
t3: R1  (R1) + (MBR)
We begin with the IR containing the ADD instruction.
In the first step, the address portion of the IR is loaded into the MAR.
Then the referenced memory location is read.
Finally, the contents of R1 and MBR are added by the ALU.
Again, this is a simplified example. Additional micro-operations may be required to extract the register reference from the IR and perhaps to stage the ALU inputs or outputs in some intermediate registers.

## Slide 10
t1: MAR  (IR(address))
t2: MBR  Memory
t3: R1  (R1) + (MBR)
ADD R1, X

## Slide 11: Figure 19.3 Flowchart for Instruction Cycle
Notes: We have seen that each phase of the instruction cycle can be decomposed into a sequence of elementary micro-operations.
In our example, there is one sequence each for the fetch, indirect, and interrupt cycles, and, for the execute cycle, there is one sequence of micro-operations for each opcode.
To complete the picture, we need to tie sequences of micro-operations together, and this is done in Figure 19.3.
We assume a new 2-bit register called the instruction cycle code (ICC). The ICC designates the state of the processor in terms of which portion of the cycle it is in:
00: Fetch
01: Indirect
10: Execute
11: Interrupt
At the end of each of the four cycles, the ICC is set appropriately.
The indirect cycle is always followed by the execute cycle.
The interrupt cycle is always followed by the fetch cycle (see Figure 16.3, (The Instruction Cycle ).
For both the fetch and execute cycles, the next cycle depends on the state of the system.
Thus, the flowchart of Figure 19.3 defines the complete sequence of micro-operations, depending only on the instruction sequence and the interrupt pattern.
Of course, this is a simplified example. The flowchart for an actual processor would be more complex.
In any case, we have reached the point in our discussion in which the operation of the processor is defined as the performance of a sequence of micro-operations. We can now consider how the control unit causes this sequence to occur.

## Slide 12: Control Unit Functional Requirements
By reducing the operation of the processor to its most fundamental level we are able to define exactly what it is that the control unit must cause to happen
Three step process to lead to a characterization of the control unit:
  Define basic elements of processor
  Describe micro-operations processor performs
  Determine the functions that the control unit must perform to cause the micro-operations to be performed
The control unit performs two basic tasks:
  Sequencing
  Execution
Notes: As a result of our analysis in the preceding section, we have decomposed the behavior or functioning of the processor into elementary operations, called micro-operations.
By reducing the operation of the processor to its most fundamental level, we are able to define exactly what it is that the control unit must cause to happen.
Thus, we can define the functional requirements for the control unit: those functions that the control unit must perform.
A definition of these functional requirements is the basis for the design and implementation of the control unit.
With the information at hand, the following three-step process leads to a characterization of the control unit:
1. Define the basic elements of the processor.
2. Describe the micro-operations that the processor performs.
Determine the functions that the control unit must perform to cause the micro-operations to be performed.
We have already performed steps 1 and 2. Let us summarize the results. First,the basic functional elements of the processor are the following:
■ ALU
■ Registers
■ Internal data paths
■ External data paths
■ Control unit
Some thought should convince you that this is a complete list.
The ALU is the functional essence of the computer.
Registers are used to store data internal to the processor. Some registers contain status information needed to manage instruction sequencing (e.g., a program status word).
Others contain data that go to or come from the ALU, memory, and I/O modules.
Internal data paths are used to move data between registers and between register and ALU.
External data paths link registers to memory and I/O modules, often by means of a system bus.
The control unit causes operations to happen within the processor.
The execution of a program consists of operations involving these processor elements. As we have seen, these operations consist of a sequence of micro-operations. Upon review of Section 19.1, the reader should see that all micro-operations fall into one of the following categories:
■ Transfer data from one register to another.
■ Transfer data from a register to an external interface (e.g., system bus).
■ Transfer data from an external interface to a register.
■ Perform an arithmetic or logic operation, using registers for input and output.
All of the micro-operations needed to perform one instruction cycle, including all of the micro-operations to execute every instruction in the instruction set, fall into one of these categories.
We can now be somewhat more explicit about the way in which the control unit functions. The control unit performs two basic tasks:
■ Sequencing: The control unit causes the processor to step through a series of micro-operations in the proper sequence, based on the program being executed.
■ Execution: The control unit causes each micro-operation to be performed.
The preceding is a functional description of what the control unit does. The key to how the control unit operates is the use of control signals.

## Slide 13: Figure 19.4 Block Diagram of the Control Unit
Notes: We have defined the elements that make up the processor (ALU, registers, data paths) and the micro-operations that are performed.
For the control unit to perform its function,
it must have inputs that allow it to determine the state of the system
and outputs that allow it to control the behavior of the system.
These are the external specifications of the control unit.
Internally, the control unit must have the logic required to perform its sequencing and execution functions.
We defer a discussion of the internal operation of the control unit to Section 19.3 and Chapter 19.4.
The remainder of this section is concerned with the interaction between the control unit and the other elements of the processor.
Figure 19.4 is a general model of the control unit, showing all of its inputs and outputs. The inputs are:
■ Clock: This is how the control unit “keeps time.” The control unit causes one micro-operation (or a set of simultaneous micro-operations) to be performed for each clock pulse.
This is sometimes referred to as the processor cycle time, or the clock cycle time.
■ Instruction register: The opcode and addressing mode of the current instruction are used to determine which micro-operations to perform during the execute cycle.
■ Flags: These are needed by the control unit to determine the status of the processor and the outcome of previous ALU operations.
For example, for the Increment-and-skip-if-zero (ISZ) instruction, the control unit will increment the PC if the zero flag is set.
■ Control signals from control bus: The control bus portion of the system bus provides signals to the control unit.
The outputs are as follows:
■ Control signals within the processor: These are two types: those that cause data to be moved from one register to another, and those that activate specific ALU functions.
■ Control signals to control bus: These are also of two types: control signals to memory, and control signals to the I/O modules.
Three types of control signals are used: those that activate an ALU function; those that activate a data path; and those that are signals on the external system bus or other external interface.
All of these signals are ultimately applied directly as binary inputs to individual logic gates.
Let us consider again the fetch cycle to see how the control unit maintains control.
The control unit keeps track of where it is in the instruction cycle.
At a given point, it knows that the fetch cycle is to be performed next.
The first step is to transfer the contents of the PC to the MAR.
  The control unit does this by activating the control signal that opens the gates between the bits of the PC and the bits of the MAR.
  The next step is to read a word from memory into the MBR and increment the PC.
  The control unit does this by sending the following control signals simultaneously:
■ A control signal that opens gates, allowing the contents of the MAR onto the
address bus;
■ A memory read control signal on the control bus;
■ A control signal that opens the gates, allowing the contents of the data bus to
be stored in the MBR;
■ Control signals to logic that add 1 to the contents of the PC and store the
result back to the PC.
Following this, the control unit sends a control signal that opens gates between the MBR and the IR.
This completes the fetch cycle except for one thing: The control unit must decide whether to perform an indirect cycle or an execute cycle next.
To decide this, it examines the IR to see if an indirect memory reference is made.
The indirect and interrupt cycles work similarly. For the execute cycle, the control unit begins by examining the opcode and, on the basis of that, decides which sequence of micro-operations to perform for the execute cycle.

## Slide 14: Figure 19.5 Data Paths and Control Signals
Notes: To illustrate the functioning of the control unit, let us examine a simple example. Figure 19.5 illustrates the example. This is a simple processor with a single accumulator (AC). The data paths between elements are indicated.
The control paths for signals emanating from the control unit are not shown, but the terminations of control signals are labeled Ci and indicated by a circle.
The control unit receives inputs from the clock, the IR, and flags.
With each clock cycle, the control unit reads all of its inputs and emits a set of control signals. Control signals go to three separate destinations:
■ Data paths: The control unit controls the internal flow of data.
For example, on instruction fetch, the contents of the memory buffer register are transferred to the IR. For each path to be controlled, there is a switch (indicated by a circle in the figure).
A control signal from the control unit temporarily opens the gate to let data pass.
■ ALU: The control unit controls the operation of the ALU by a set of control signals. These signals activate various logic circuits and gates within the ALU.
■ System bus: The control unit sends control signals out onto the control lines of the system bus (e.g., memory READ).

## Slide 15: Table 19.1 Micro-operations and Control Signals
 | Micro-operations | Active Control Signals
Fetch: | t1: MAR ← (PC) | C2
 | t2: MBR ← Memory PC ← (PC) + 1 | C5, CR
 | t3: IR ← (MBR) | C4
Indirect: | t1: MAR ← (IR(Address)) | C8
 | t2: MBR ← Memory | C5, CR
 | t3: IR(Address) ← (MBR(Address)) | C4
Interrupt: | t1: MBR ← (PC) | C1
 | t2 : MAR ← Save-address PC ← Routine-address | 
 | t3: Memory ← (MBR) | C12, CW
CR = Read control signal to system bus.
CW = Write control signal to system bus.
(Table can be found on page 681in the textbook.)
Notes: The control unit must maintain knowledge of where it is in the instruction cycle.
Using this knowledge, and by reading all of its inputs, the control unit emits a sequence of control signals that causes micro-operations to occur.
It uses the clock pulses to time the sequence of events, allowing time between events for signal levels to stabilize.
Table 19.1 indicates the control signals that are needed for some of the micro-operation sequences described earlier.
For simplicity, the data and control paths for incrementing the PC and for loading the fixed addresses into the PC and MAR are not shown.
It is worth pondering the minimal nature of the control unit.
The control unit is the engine that runs the entire computer.
It does this based only on knowing the instructions to be executed and the nature of the results of arithmetic and logical operations (e.g., positive, overflow, etc.).
It never gets to see the data being processed or the actual results produced.
And it controls everything with a few control signals to points within the processor and a few control signals to the system bus.

## Slide 16: Figure 19.6 CPU with Internal Bus
Notes: Figure 19.5 indicates the use of a variety of data paths.
The complexity of this type of organization should be clear. More typically, some sort of internal bus arrangement, as was suggested in Figure 16.1(Internal Structure of the CPU), will be used.
Using an internal processor bus, Figure 19.5 can be rearranged as shown in Figure 19.6.
A single internal bus connects the ALU and all processor registers.
Gates and control signals are provided for movement of data onto and off the bus from each register.
Additional control signals control data transfer to and from the system (external) bus and the operation of the ALU.
Two new registers, labeled Y and Z, have been added to the organization.
These are needed for the proper operation of the ALU. When an operation involving
two operands is performed, one can be obtained from the internal bus, but the
other must be obtained from another source. The AC could be used for this purpose,
but this limits the flexibility of the system and would not work with a processor
with multiple general-purpose registers. Register Y provides temporary storage
for the other input.
The ALU is a combinatorial circuit (see Chapter 12) with no internal storage.
Thus, when control signals activate an ALU function, the input to the ALU is transformed to the output.
Therefore, the output of the ALU cannot be directly connected to the bus, because this output would feed back to the input.
Register Z provides temporary output storage.

## Slide 17: Figure 19.7 Intel 8085 CPU Block Diagram
Notes: To illustrate some of the concepts introduced thus far in this chapter, let us consider
the Intel 8085. Its organization is shown in Figure 19.7. Several key components that
may not be self-explanatory are:
■ Incrementer/decrementer address latch: Logic that can add 1 to or subtract 1 from the contents of the stack pointer or program counter. This saves time by avoiding the use of the ALU for this purpose.
■ Interrupt control: This module handles multiple levels of interrupt signals.
■ Serial I/O control: This module interfaces to devices that communicate 1 bit at a time.

## Slide 18: Control Unit Implementation
A wide variety of techniques have been used for control unit implementation
Most of these fall into two categories:
  Hardwired implementation
      The control unit is essentially a state machine circuit
      Its input logic signals are transformed into a set of output logic signals, which are the control signals
  Microprogrammed implementation
Notes: We have discussed the control unit in terms of its inputs, output, and functions. We
now turn to the topic of control unit implementation. A wide variety of techniques
have been used. Most of these fall into one of two categories:
■ Hardwired implementation
■ Microprogrammed implementation
In a hardwired implementation, the control unit is essentially a state machine
circuit. Its input logic signals are transformed into a set of output logic signals, which
are the control signals. This approach is examined in this section. Microprogrammed
implementation is the subject of Section 19.4.

## Slide 19: Table 19.3 A Decoder With 4 Inputs and 16 Outputs
I1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
I2 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
I3 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
I4 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
O1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
O2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
O3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
O4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
O5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
O6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
O7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
O8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O10 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O11 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O12 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O13 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O14 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O15 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O16 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
(Table can be found on page 687in the textbook.)
Notes: Figure 19.4 depicts the control unit as we have so far discussed it. The key inputs are
the IR, the clock, flags, and control bus signals. In the case of the flags and control
bus signals, each individual bit typically has some meaning (e.g., overflow). The other
two inputs, however, are not directly useful to the control unit.
First consider the IR. The control unit makes use of the opcode and will perform different actions (issue a different combination of control signals) for different instructions.
To simplify the control unit logic, there should be a unique logic input for each opcode.
This function can be performed by a decoder , which takes an encoded input and produces a single output.
In general, a decoder will have n binary inputs and 2n binary outputs. Each of the 2n different input patterns will activate a single unique output. Table 19.3 is an example for n = 4. The decoder for a control unit will typically
have to be more complex than that, to account for variable-length opcodes. An example of the digital logic used to implement a decoder is presented in Chapter 12.

## Slide 20: Figure 19.10 Control Unit with Decoded Inputs
Notes: The clock portion of the control unit issues a repetitive sequence of pulses.
This is useful for measuring the duration of micro-operations. Essentially, the period
of the clock pulses must be long enough to allow the propagation of signals along
data paths and through processor circuitry. However, as we have seen, the control
unit emits different control signals at different time units within a single instruction
cycle. Thus, we would like a counter as input to the control unit, with a different
control signal being used for T1 ,T2 , and so forth. At the end of an instruction cycle,
the control unit must feed back to the counter to reinitialize it at T1 .
With these two refinements, the control unit can be depicted as in Figure 19.10.

## Slide 21: Microprogrammed Control
The term microprogrammed was first coined by M.V. Wilkes in the early 1950’s
Wilkes proposed an approach to control unit design that was organized and systematic and avoided the complexities of a hardwired implementation
The idea intrigued many researchers but appeared unworkable because it would require a fast, relatively inexpensive control memory
In April of 1964 IBM’s System/360 was announced and all but the largest models were microprogrammed
Microprogramming became a popular technique for implementing the control unit of CISC processors
In recent years, microprogramming has become less used but remains a tool available to computer designers
Notes: The term microprogram was first coined by M. V. Wilkes in the early 1950s [WILK51].
Wilkes proposed an approach to control unit design that was organized and systematic
and avoided the complexities of a hardwired implementation. The idea intrigued
many researchers but appeared unworkable because it would require a fast, relatively
inexpensive control memory.
The state of the microprogramming art was reviewed by Datamation in its
February 1964 issue. No microprogrammed system was in wide use at that time,
and one of the papers [HILL64] summarized the then-popular view that the future
of microprogramming “is somewhat cloudy. None of the major manufacturers has
evidenced interest in the technique, although presumably all have examined it.”
This situation changed dramatically within a very few months. IBM’s System/
360 was announced in April, and all but the largest models were microprogrammed.
Although the 360 series predated the availability of semiconductor
ROM, the advantages of microprogramming were compelling enough for IBM
to make this move. Microprogramming became a popular technique for implementing
the control unit of CISC processors. In recent years, microprogramming
has become less used but remains a tool available to computer designers.
For example, as we have seen on the Pentium 4, machine instructions are converted
into a RISC-like format, most of which are executed without the use
of microprogramming. However, some of the instructions are executed using
microprogramming.

## Slide 22
Microprogramming Language
The notation used in Table 19.1 looks suspiciously like a programming language.
Each line describes a set of micro-operations occurring at one time and is known as a microinstruction.
A sequence of instructions is known as a microprogram, or firmware.
This latter term reflects the fact that a microprogram is midway between hardware and software.

## Slide 23: Table 19.1 Micro-operations and Control Signals
 | Micro-operations | Active Control Signals
Fetch: | t1: MAR ← (PC) | C2
 | t2: MBR ← Memory PC ← (PC) + 1 | C5, CR
 | t3: IR ← (MBR) | C4
Indirect: | t1: MAR ← (IR(Address)) | C8
 | t2: MBR ← Memory | C5, CR
 | t3: IR(Address) ← (MBR(Address)) | C4
Interrupt: | t1: MBR ← (PC) | C1
 | t2 : MAR ← Save-address PC ← Routine-address | 
 | t3: Memory ← (MBR) | C12, CW
CR = Read control signal to system bus.
CW = Write control signal to system bus.
(Table can be found on page 681in the textbook.)

## Slide 24: Control Word
For each micro-operation, all that the control unit is allowed to do is generate a set of control signals.
Thus, for any micro-operation, each control line emanating from the control unit is either on or off.
This condition can be represented by a binary digit for each control line. So we could construct a control word in which each bit represents one control line.
Each micro-operation would be represented by a different pattern of 1s and 0s in the control word

## Slide 25: Control Memory
The sequence of micro-operations performed by the control unit is represented by a sequence of control words.
Each stage of the instruction cycle has a different sequence of micro-operations.
Store the control words in a memory, with each word having a unique address.

## Slide 26: Figure 19.13 Organization of Control Memory
Notes: Figure 19.13 shows how these control words or microinstructions could be arranged in a control memory . The microinstructions in each routine are to be executed sequentially. Each routine ends with a branch or jump instruction indicating where to go next. There is a special execute cycle routine whose only purpose is to signify that one of the machine instruction routines (AND, ADD, and so on) is to be executed next, depending on the current opcode.
The control memory of Figure 19.13 is a concise description of the complete
operation of the control unit. It defines the sequence of micro-operations to be
performed during each cycle (fetch, indirect, execute, interrupt), and it specifies the
sequencing of these cycles. If nothing else, this notation would be a useful device
for documenting the functioning of a control unit for a particular computer. But it is
more than that. It is also a way of implementing the control unit.

## Slide 27: Figure 19.12 Typical Microinstruction Formats
Notes: How can we use the concept of microprogramming to implement a control unit? Consider that for each micro-operation, all that the control unit is allowed to do is generate a set of control signals. Thus, for any micro-operation, each control line emanating from the control unit is either on or off. This condition can, of course, be represented by a binary digit for each control line. So we could construct a control word in which each bit represents one control line. Then each micro-operation would be represented by a different pattern of 1s and 0s in the control word.
Suppose we string together a sequence of control words to represent the
sequence of micro-operations performed by the control unit. Next, we must recognize
that the sequence of micro-operations is not fixed. Sometimes we have an
indirect cycle; sometimes we do not. So let us put our control words in a memory,
with each word having a unique address. Now add an address field to each control
word, indicating the location of the next control word to be executed if a certain
condition is true (e.g., the indirect bit in a memory-reference instruction is 1). Also,
add a few bits to specify the condition.
The result is known as a horizontal microinstruction, an example of which
is shown in Figure 19.12a. The format of the microinstruction or control word is as follows.
There is one bit for each internal processor control line and one bit for each system bus control line.
There is a condition field indicating the condition under which there should be a branch, and
there is a field with the address of the microinstruction to be executed next when a branch is taken.
Such a microinstruction is interpreted as follows:
1. To execute this microinstruction, turn on all the control lines indicated by a 1 bit; leave off all control lines indicated by a 0 bit. The resulting control signals will cause one or more micro-operations to be performed.
2. If the condition indicated by the condition bits is false, execute the next microinstruction in sequence.
3. If the condition indicated by the condition bits is true, the next microinstruction to be executed is indicated in the address field.

## Slide 28: Figure 19.14 Control Unit Microarchitecture
Notes: The control memory of Figure 19.13 contains a program that describes the behavior of the control unit. It follows that we could implement the control unit by simply executing that program.
Figure 19.14 shows the key elements of such an implementation.
The set of microinstructions is stored in the control memory .
The control address register contains the address of the next microinstruction to be read.
When a microinstruction is read from the control memory, it is transferred to a control buffer register.
  The lefthand portion of that register (see Figure 19.12a) connects to the control lines emanating from the control unit.
  Thus, reading a microinstruction from the control memory is the same as executing that microinstruction.
The third element shown in the figure is a sequencing unit that loads the control address register and issues a read command.

## Slide 29: Figure 19.15 Functioning of Microprogrammed Control Unit
Notes: Let us examine this structure in greater detail, as depicted in Figure 19.15. Comparing this with Figure 19.14, we see that the control unit still has the same inputs (IR, ALU flags, clock) and outputs (control signals). The control unit functions as follows:
1. To execute an instruction, the sequencing logic unit issues a READ command to the control memory.
2. The word whose address is specified in the control address register is read into the control buffer register.
3. The content of the control buffer register generates control signals and next-address information for the sequencing logic unit.
4. The sequencing logic unit loads a new address into the control address register based on the next-address information from the control buffer register and the ALU flags.
All this happens during one clock pulse.
The last step just listed needs elaboration.
At the conclusion of each microinstruction, the sequencing logic unit loads a new address into the control address register.
Depending on the value of the ALU flags and the control buffer register, one of three decisions is made:
■ Get the next instruction: Add 1 to the control address register.
■ Jump to a new routine based on a jump microinstruction: Load the address field of the control buffer register into the control address register.
■ Jump to a machine instruction routine: Load the control address register based on the opcode in the IR.
Figure 19.15 shows two modules labeled decoder .
The upper decoder translates the opcode of the IR into a control memory address.
The lower decoder is not used for horizontal microinstructions but is used for vertical microinstructions
(Figure 19.12b). As was mentioned, in a horizontal microinstruction every bit in the control field attaches to a control line.
In a vertical microinstruction, a code is used for each action to be performed [e.g., MAR  (PC)], and the decoder translates this code into individual control signals. The advantage of vertical microinstructions
is that they are more compact (fewer bits) than horizontal microinstructions, at the expense of a small additional amount of logic and time delay.

## Slide 30: Figure 19.16 Wilkes’s Microprogrammed Control Unit
Notes: As was mentioned, Wilkes first proposed the use of a microprogrammed control unit in 1951 [WILK51]. This proposal was subsequently elaborated into a more detailed design [WILK53]. It is instructive to examine this seminal proposal.
The configuration proposed by Wilkes is depicted in Figure 19.16.
The heart of the system is a matrix partially filled with diodes.
During a machine cycle, one row of the matrix is activated with a pulse.
This generates signals at those points where a diode is present (indicated by a dot in the diagram).
The first part of the row generates the control signals that control the operation of the processor.
The second part generates the address of the row to be pulsed in the next machine cycle.
Thus, each row of the matrix is one microinstruction, and the layout of the matrix is the control memory.
At the beginning of the cycle, the address of the row to be pulsed is contained in Register I.
This address is the input to the decoder, which, when activated by a clock pulse, activates one row of the matrix.
Depending on the control signals, either the opcode in the instruction register or the second part of the pulsed row is passed into Register II during the cycle.
Register II is then gated to Register I by a clock pulse.
Alternating clock pulses are used to activate a row of the matrix and to transfer from Register II to Register I.
The two-register arrangement is needed because the decoder is simply a combinatorial circuit; with only one register, the output would become the input during a cycle, causing an unstable condition.
This scheme is very similar to the horizontal microprogramming approach
described earlier (Figure 19.12a). The main difference is this: In the previous description, the control address register could be incremented by one to get the next address. In the Wilkes scheme, the next address is contained in the microinstruction.
To permit branching, a row must contain two address parts, controlled by a
conditional signal (e.g., flag), as shown in the figure.
Having proposed this scheme, Wilkes provides an example of its use to implement
the control unit of a simple machine. This example, the first known design of a
microprogrammed processor, is worth repeating here because it illustrates many of
the contemporary principles of microprogramming.

## Slide 31
Notes: Therefore, all of the characteristics listed in Table 21.4 fall along a spectrum of design strategies. In general, a design that falls toward the left end of the spectrum is intended to optimize the performance of the control unit. Designs toward the right end are more concerned with optimizing the process of microprogramming.
Indeed, microinstruction sets near the right end of the spectrum look very much like machine instruction sets. A good example of this is the LSI-11 design, described later in this section. Typically, when the objective is simply to implement a control unit, the design will be near the left end of the spectrum. The IBM 3033 design, discussed presently, is in this category. As we shall discuss later, some systems permit a variety of users to construct different microprograms using the same microinstruction facility.
In the latter cases, the design is likely to fall near the right end of the spectrum.
We can now deal with some of the terminology introduced earlier. Table 21.4 indicates how three of these pairs of terms relate to the microinstruction spectrum. In essence, all of these pairs describe the same thing but emphasize different design characteristics.
The degree of packing relates to the degree of identification between a given control task and specific microinstruction bits.
  As the bits become more packed, a given number of bits contains more information. Thus, packing connotes encoding.
The terms horizontal and vertical relate to the relative width of microinstructions.
  [SIEW82] suggests as a rule of thumb that vertical microinstructions have lengths in the range of 16 to 40 bits and that horizontal microinstructions have lengths in the range of 40 to 100 bits.
The terms hard and soft microprogramming are used to suggest the degree of closeness to the underlying control signals and hardware layout.
  Hard microprograms are generally fixed and committed to read-only memory.
  Soft microprograms are more changeable and are suggestive of user microprogramming.

## Slide 32: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructions in teaching their courses and assessing student learning. dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permit- ted. The work and materials from it should never be made available to
students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these
restrictions and to honor the intended pedagogical purposes and the needs of
other instructors who rely on these materials.